## Slide 2: HOSPITAL WASTE MANAGEMENT Block 2 Opthalmology
Dr Mehwish Riaz
Dr.Narjis Zaidi

## Slide 3
Wisdom
Truth
Service
To impart evidence based research oriented medical education
To provide best possible patient care
To inculcate the values of mutual respect and ethical practice of medicine
Vision & Mission of RMU

## Slide 4: Prof Umar Model

## Slide 5: Sequence Of Lecture
Statement of learning outcomes (01 slide)
Core Subject ( 15 )
Vertical integration ( 03 )
Horizotal integration (01)
EOLA(End of lecture assessment)( 01)
Digital Library References
Research, Bioethics, Artificial Intelligence) ( 01)

## Slide 6: Learning Objectives
At the end students are able to:
Define hospital waste and biomedical waste
Describe its classification and health risk associated with waste
Describe its composition and source
Explain different people at risk and management
Describe waste management hierarchy
Enlist steps of segregation and handling

## Slide 7
DEFINITION
Hospital waste is any waste which is generated in the diagnosis, treatment or immunization of human beings or animals or in research” in a hospital. This is also called ‘Bio-Medical Waste’ (BMW).
Hospital Waste Management means the management of waste produced by hospitals using such techniques that will help to check the spread of diseases through.
“Bio-medical waste” means any waste, which is generated during the diagnosis, treatment or immunization of human beings or animals or in research activities.
Core Content

## Slide 8: Classification of Hospital Waste
Non-Hazardous:
Hazardous:
Core Content

## Slide 9
Core Content

## Slide 10: Composition:
Core Content

## Slide 11: Medical Waste Generation in Asia
Developing Countries: 1-2 kg/patient/day
https://nswai.org/docs/Medical%20Waste%20Management%20Issues%20in%20India.pdf
Core Content

## Slide 12: Health Risks from Poor Hospital Waste Management
Vertical integration

## Slide 13: Pathological Hospital Waste
Pathological waste includes any detached human or animal organs, tissues, and body parts including body parts used in research but does not include teeth. Waste materials from a biopsy procedure are an example of pathological biohazardous waste.
Horizontal integration

## Slide 14: Who are at risk
Medical Staff : Doctors, Nurses, sanitary workers,hospital maintenance personnel
Visitors Of patients
House Keepers
Infection Control team
Community
Vertical integration

## Slide 15: Management of Healthcare Waste
National Policy & Strategy with Guidelines and SOP
Legislation/ Rules for waste management
Political commitment
Committed manpower
Good Management
Proper budgetary allocation
Effective Waste Management needs:
Core Content

## Slide 16: Health hazards of hospital waste
HIV
Hepatitis
Tuberculosis
pneumonia
diarrhoea
tetanus
whooping cough etc. are other common diseases spread due to improper waste management.
2nd in disease burden of Hepatitis B and C globally
(The greatest risk factors for HCV transmission include blood transfusions (15%), history of hospitalization (14%), dental treatment (13%), use of injections (12%), and history of surgery (9%).21-Jun-2022)
Vertical integration

## Slide 17: Waste Management Hierarchy
Core Content

## Slide 18: WHO Hospital Waste Management Cycle
Core Content

## Slide 19: Steps in Management of Hospital Waste
Steps in the management of hospital waste include : -
Training and Awareness
Generation
Segregation / separation
Collection
Transportation
Storage
Treatment
Final disposal
Core Content

## Slide 20
WASTE MANAGEMENT TEAM
This includes:
Medical supervisor
Head of each department
Infection control officer
Chief pharmacists
Radiology officer
Senior matron
Hospital engineer
Core Content

## Slide 21: Waste Minimization & Identification
Waste minimization is a process of elimination that involves reducing the amount of waste produced in society and helps to eliminate the generation of harmful and persistent wastes.
An appropriate way of identifying the waste is by sorting the waste into different colour code.
Colour code is easy for identification and thereby easy for safe handling, transportation and waste treatment. The colour code varies country to country.
Core Content

## Slide 22: WHO Recommended Colour Code
Core Content

## Slide 23
Core Content

## Slide 24: Waste Collection & Transportation
Collectors must wear protective materials
Collection of waste in coloured bags or coloured covered bins
Content of the container should not exceed three quaters of its capacity
If bag of waste is used , tie the neck tightly
Avoid throwing and dragging over the floor
Transportation of waste by designated trolleys from site of origin to temporary storage area. Should not be store more than 24 hours.
Core Content

## Slide 25: Treatment / Disposal technologies for health care waste
Incineration
Chemical disinfection
Wet and dry thermal treatment
Microwave irradiation
Land disposal
Inertization
Core Content

## Slide 26
Core Content

## Slide 27: Incineration
Incineration is a high temperature dry oxidation process, that reduces organic and combustible waste to inorganic incombustible matter and results in a very significant reduction of waste-volume and weight. The process is usually selected to treat wastes that cannot be recycled, reused or disposed off in a land fill site.
Characteristics of the waste suitable for incineration are:
Low heating volume (2000- 3500 kcal/kg)
Content of combustible matter above 60 %
Content of noncombustible solids below 5 %
Content of noncombustible fines below 20 %
Moisture content below 30 %
Core Content

## Slide 28
Waste types not to be incinerated are:
Pressurized gas containers
Large amount of reactive chemical wastes
Silver salts and radiographic wastes
Halogenated plastics such as PVC
Waste with high mercury or cadmium content (broken thermometers, used batteries)
Sealed ampoules or ampoules containing heavy metals
Core Content

## Slide 29: Chemical disinfection
Chemicals are added to waste to kill or inactivate the pathogens it contains. Chemical disinfection is most suitable for treating liquid waste such as blood, urine, stools or hospital sewage. This treatment usually results in disinfection rather than sterilization.
Wet & dry thermal treatment
Wet thermal treatment is based on exposure of shredded infectious waste to high temperature, high pressure steam, and is similar to the autoclave sterilization process.
In dry thermal treatment waste is shredded and heated in a rotating auger. The waste is reduced by 80 % in volume. This process is suitable for treating infectious waste and sharps.
Core Content

## Slide 30: Inertization
The process of “Inertization” involves mixing waste with cement and other substances before disposal, in order to minimize the risk of toxic substances contained in the wastes migrating into the surface water or ground water. A typical proportion of the mixture is:
65 % pharmaceutical waste
15 % lime
15 % cement
5 % water
A homogeneous mass is formed and cubes or pellets are produced on site and then transported to suitable storage sites.
Core Content

## Slide 31: PERSONAL PROTECTIVE EQUIPMENT (PPE)
PPE
Heavy duty gloves.
Industrial boot.
Industrial apron or leg protector.
Eye protectors, masks,
over alls.
Helmets with visors and dust masks.
USE
Protect hand when moving bags.
Protect feet against spillage of sharp.
Protect against bodily contact.
To protect the body in accident and spillage clear up operations .
To protect incinerator operators when loading incinerators manually or when removing ash for disposal.
Core Content

## Slide 32: Current practices of waste management in teaching hospitals and presence of incinerators in densely populated areas
RESEARCH
https://bmcpublichealth.biomedcentral.com/articles/10.1186/s12889-021-11389-1

## Slide 33: Hospital Waste Management in theTeaching Hospitals of Karachi
RESEARCH

## Slide 34: OSPE
a. Classify hospital waste.
b. Which kind of waste is disposed in red and yellow bin?

## Slide 35: MCQs
The color code of plastic bag for disposing of microbial laboratory culture waste in a tertiary care hospital of pakistan is:
a) Black
b) Red
c) Blue
d) White
c) Yellow
Answer: b

## Slide 36: Digital Library
https://www.env.go.jp/recycle/3r/en/asia/02_03-2/04.pdf
https://nswai.org/docs/Medical%20Waste%20Management%20Issues%20in%20India.pdf
https://www.env.go.jp/recycle/3r/en/asia/02_03-2/05.pdf

## Slide 37: Research & Ethics
https://pubmed.ncbi.nlm.nih.gov/26628050/

## Slide 38: Research & Ethics
https://bmcpublichealth.biomedcentral.com/articles/10.1186/s12889-021-11389-1

## Slide 39
Thank You